## Slide 1
Title : Identification of 8-inch & 10.25-inch DA Unit
Check visually system to identify Buttons of 8-inch unit are on the right side and buttons of 10.25-inch unit are on the bottom side.
ANNEXURE- 1
Software for 8-inch and 10.25-inch DA are different. Select Software for installation basis physical unit in car
8-inch DA Unit
10.25-inch DA Unit

## Slide 2
ANNEXURE- 2
Title : Preparation of the USB
Download the software files from below link.
  8-inch DA file name : update-Ver01.000.200-work10_size8
  10.25-inch DA file name : update-Ver01.000.201-work10_size10 2
software files from zip folder.
Format the USB as
  File system : FAT32
  Allocation Size : 4096 bytes
Transfer the relevant software files to USB device. USB device should not contain any other files.
8-inch DA Unit
10.25-inch DA Unit

## Slide 3
No. | Description | Details
1 | Switch on the ignition | 
2 | Select ‘Ok’ from caution screen | 
3 | Press ‘Setting’ button Flick screen to left | 
4 | Select the “About”. | 
ANNEXURE- 3
Title : Software Version Check procedure

## Slide 4
ANNEXURE- 3
No. | Description | Details
5 | Observe “SYSTEM Version” | 
7 | Observe “SYSTEM Version” | 
Title : Software Version Check procedure

## Slide 5
ANNEXURE- 3
No. | Description | Details
8 | Updated “SYSTEM Version” | 
Title : Software Version Check procedure
8-inch DA Unit
Version : 01.000.600
10.25-inch DA Unit
Version: 01.000.601

## Slide 6
ANNEXURE- 4
Title : Software Update procedure
No. | Description | Details
1 | Switch on the ignition | 
2 | Caution screen will appear. Select “OK”. | 
3 | Insert USB in port as shown in fig | 
4 | Pop will appear for software update. Select “Yes” . | 
Please do not cut off power supply during boot upgrading,
otherwise, the H/U may be damaged and cannot be repaired.

## Slide 7
ANNEXURE- 4
Title : Software Update procedure
No. | Description | Details
5 | Software update will start. Audio Unit will reboot during the process. “Software Update Compete. The USB device can now be disconnected. The System will restart after 5 seconds” message will appear. | 

## Slide 8
ANNEXURE- 4
Title : Software Update procedure
No. | Description | Details
6 | Switch off the vehicle | 
7 | Remove USB device from port | 
1. In case of fail during update. Please turn off ACC around 15 sec. and retry in first step again.